## Slide 1
The Work Left to Do
Model estimates
What we observe
Nitrogen reductions still needed (estimated by CBP):
32 million pounds/yr
Annual rate of nonpoint source N reductions since TMDL (2009)
0.3 million pounds/yr
Goal
Model estimates
Monitored
In some areas, we have more work to do than we think

## Slide 2
 | Nitrogen |  |  | Phosphorus |  | 
River Input Monitoring Stations | CAST change in load | Change monitor load | Does CAST fall outside 90% CI? | CAST change in load | Change monitor load | Does CAST fall outside 90% CI?
Susquehanna | -3% | -4% | No | 21% | 29% | No
Potomac | -11% | -13% | No | -11% | 10% | No
James River | 11% | 3% | No | -15% | 3% | No
Rappahannock | -16% | 13% | Yes | -46% | 57% | Yes
Appomattox | 11% | 22% | Yes | 5% | 22% | Yes
Pamunkey | -9% | 14% | Yes | -23% | 23% | Yes
Mattaponi | 6% | 16% | Yes | 19% | 5% | Yes
Patuxent | -33% | -32% | No | -29% | -21% | No
Choptank | -1% | 20% | Yes | 29% | 95% | Yes
Outcomes we observe
Example: Phosphorus in the Choptank
Notes: Response gap. Estimates of nutrient load reductions relative to monitored loads by major bay tributaries (1995-2020), calculated by comparing the dynamic CAST model estimated TN and TP loads against flow-normalized observed load* (WRTDS- weighted regression on time discharge and season) with 90% confidence interval (CI) calculated. Bold values present conditions where CAST estimates fall outside of the WRTDS-CI estimate. (Source: Monitored and Expected Total Reduction Indicator for the Chesapeake-METRIC, 2024).
Example of the phosphorus response gap for the Choptank River MD and Potomac River, MD. WIP -Watershed Implementation Plan, CI - Confidence Interval. (Source: Monitored and Expected Total Reduction Indicator for the Chesapeake-METRIC, 2024).

## Slide 3
Mass Balance: What goes "in" must come "out" or get "stored"
Farm Nutrient Mass Balance
Nutrient Imports
Nutrient Exports
FARM
Surplus
Storage (soils, GW, biota)
Export to Water & Atmosphere (N)
Feed
Fertilizer
Other
Imports
Animal
Milk
Crops
Animal
Other
Exports
Urban BMP:
Bioretention
Nutrients in runoff
Other
Exports
To water
Storage
Nutrient Imports
Nutrient Exports
Water & Atmosphere (N)
Mass Balance for Urban BMP

## Slide 4
0.00 – 0.03
0.04 – 0.06
0.07 – 0.09
0.10 – 0.12
0.13 – 0.15
0.16 – 0.18
0.19 – 0.21
0.22 – 0.24
> 0.24
0.0 – 1.0
1.1 – 2.0
2.1 – 3.0
3.1 – 4.0
4.1 – 5.0
5.1 – 6.0
6.1 – 7.0
7.1 – 8.0
> 8.0
Delivered Nitrogen (kg/ha/yr)
Delivered Phosphorus (kg/ha/yr)
What areas are contributing the most nutrients loads?

## Slide 5
0 – 1
1 – 2
2 – 5
5 – 10
10 – 20
10 – 50
>50
Missing
0 – 1
1 – 2
2 – 5
5 – 10
10 – 20
10 – 50
>50
Missing
2019 Agricultural TP
Surplus (kg/ha)
2019 Agricultural TN
Surplus (kg/ha)
Mass Balance: Areas with Surplus Phosphorus and Nitrogen

## Slide 6
Phosphorous
Nitrogen
Notes: High TP and TN losses are associated with large nutrient surpluses
Decreasing water quality trends likewise associated with surpluses

## Slide 7
Intensive monitoring and BMP implementation
Dominated by livestock agriculture
Significant, increasing nutrient mass imbalance
Legacy nutrients in soils and groundwater contribute to lag times in water quality response
CBP showcase watershed: Smith Creek, VA
Nitrogen
Phosphorus
Notes: Smith Creek illustrates the “response gap”, where management actions do not yield expected water quality improvements.
Highlights the need for targeted interventions, mass balance management, and outcome-based incentives.

## Slide 8
CAST, BMPs, and Mass Balance
BMP
Model
State reporting
Watershed planning and Implementation Programs
Cost share
(% of BMP cost)
Adoption
Predictions of Pollutant reduction outcomes
$ offer
What is counted
CAST Accounting
What isn't

## Slide 9: A way forward….. Directing Investments
Nutrient Mass Balance (kg/ha)
# of Farms
-
0
+
Large Nutrient Surplus
Watershed to
Farm

## Slide 10: A way forward….. Measuring Progress
Moves program closer to measuring outcomes, not effort (practices)
Can be used at different scales to identify opportunities for nutrient reduction
Comprehensive picture of nutrient flows
Direct benefits to management entity (improved nutrient use efficiency)
Farm Nutrient Mass Balance
Nutrient Imports
Nutrient Exports
FARM
Surplus
Storage (soils, GW, biota)
Export to Water & Atmosphere (N)
Feed
Fertilizer
Other
Imports
Animal
Milk
Crops
Animal
Other
Exports

## Slide 11: A way forward….. Improving Incentives
Pays Virginia dairies for the amount of N surplus reduced
Aligns financial incentive with desired environmental outcome
Encouraging flexibility and innovation
Creates verifiable and auditable metric using routine farm data